## Slide 1: PicoFramework
A lightweight application framework for Raspberry Pi Pico W and Pico 2 W

## Slide 2: What is PicoFramework?
A structured C++ framework for embedded development on RP2040
Inspired by modern web frameworks (e.g., Express.js, Nest.js and similar products)
Ideal for building networked, event-driven IoT applications
Open source, MIT license for any use

## Slide 3: Why PicoFramework?
Inspired by application frameworks like Express.js, Nest.js for javascript and frameworks like Laravel for php
Microcontrollers’ limited flash and RAM has historically made it hard to replicate smaller devices
The Pico and particularly the Pico 2 have no major limitations on flash and available RAM is enough to support an application framework
Although the Pico SDK is extensive it does not have the mature higher- level components such as out-of-the box HTTP handling in the manner of the ESP32, and it has a strong bare-metal focus
PicoFramework is the first real framework for multitasking application development on microcontrollers in the style of highly capable application frameworks like Express.js

## Slide 4: Designed for:
IoT controllers (e.g., irrigation, HVAC, lighting)
Network-connected sensors and edge devices
Rapid prototyping of connected hardware
Familiarity for C++ developers
Design architecture that is easily understandable
Extensibility

## Slide 5: Features at a Glance
MVC-style application structure
HTTP server with routing and middleware
JWT authorization and token generation, password hashing
Http Client with fluent builder style requests
Event-driven system with task scheduler
Sd Card storage manager with persistent json support

## Slide 6: PicoFramework Components
Comprehensive but light framework

## Slide 7: Embedded MVC
Model – stores app config (e.g. schedules)
View – serves HTML/JS from SD card (or your own StorageManager like littleFs)
Controller – handles requests and logic
Inspired by Express.js, adapted for C++

## Slide 8: The App
App::App(int port) : FrameworkApp(port, "AppTask", 2048, 1), controller(nullptr), scheduler(nullptr)
{
std::cout << "App constructed" << std::endl;
}
void App::initRoutes() {
router.addRoute("GET", "/api/v1/programs", [this](HttpRequest &req, HttpResponse &res, const std::vector<std::string> &params)
{
  this->scheduler->handle_get_programs(req, res, params);
  });
  …
void App::run() {
waitFor(FrameworkNotification::NetworkReady);
controller = Controller::get_instance();
controller->start();
scheduler = Scheduler::get_instance();
scheduler->start();
initRoutes();
server.start()
while (true) {// app loop}

## Slide 9: Routing System (Express.js-style)
Add routes via router.addRoute(method, path, handler)
REST-friendly: GET, POST, PUT, DELETE
Lambdas or method pointers as handlers
Per-route and global middleware
Path parsing and matching with variables
Built-in /auth route handler for JWT token test (can override)
Route debug printing (adding, handling routes)
router.addRoute("GET", "/info", [](Request &req, Response &res) { res.sendText("System Info Page"); });
router.addRoute("POST", "/config", configHandler, {authMiddleware});

## Slide 10: Routing Example
Add routes in your app controller:
router.use(loggingMiddleware);
router.addRoute("GET", "/index.html", [this](HttpRequest &req, HttpResponse &res, const std::vector<std::string> &params) {
this->router.serveStatic(req, res, params);
}); router.addRoute("GET", "/api/v1/programs", [this](HttpRequest &req, HttpResponse &res, const std::vector<std::string> &params) {
this->scheduler->handle_get_programs(req, res, params);
}); router.addRoute("GET", "/api/v1/programs/{name}", [this](HttpRequest &req, HttpResponse &res, const std::vector<std::string> &params) {
this->scheduler->handle_get_program(req, res, params);
}); router.addRoute("GET", "/api/v1/zones", [this](HttpRequest &req, HttpResponse &res, const std::vector<std::string> &params) {
this->controller->handle_get_zones(req, res, params);
}); router.addRoute("POST", "/api/v1/programs", [this](HttpRequest &req, HttpResponse &res, const std::vector<std::string> &params) {
this->scheduler->handle_add_program(req, res, params);
}); router.addRoute("PUT", "/api/v1/programs/{name}", [this](HttpRequest &req, HttpResponse &res, const std::vector<std::string> &params) {
this->scheduler->handle_update_program(req, res, params);
}); router.addRoute("DELETE", "/api/v1/programs/{name}", [this](HttpRequest &req, HttpResponse &res, const std::vector<std::string> &params) {
this->scheduler->handle_delete_program(req, res, params);
});

## Slide 11: Response Handling
res.setStatus(401).send("{\"error\":\"Unauthorized\"}");
Or via helper
JsonResponse::sendError(res, 401, "INALID_TOKEN", "Invalid token");
void sendError(HttpResponse& res, int statusCode, const std::string& code, const std::string& message) {
  json j = {
    {"success", false},
    {"error", {
    {"code", code},
    {"message", message}
  }}
  };
res.status(statusCode).json(j);
}

## Slide 12: Middleware and Auth
Support for per-route and global middleware:
router.addRoute(GET, "/auth", authMiddleware, &AuthController::handle);
JWT-based authentication with token verification and generation
Optional at build time via PICO_HTTP_ENABLE_JWT

## Slide 13: JWT Authentication
Middleware-based token checking
Authorization: Bearer <jwt> parsing
HMAC signature validation
[Token expiry verification]
Protected route support with fallback 401 response
JWT secret from build or config

## Slide 14: Controller Example
[this needs updating]
void ZoneController::start(HttpRequest& req, HttpResponse& res) {
auto name = req.getPathParam("name");
zoneService.startZone(name);
res.sendJson({{"status", "started"}});
}

## Slide 15: Event System
[check event names]
Post and subscribe to system-wide events
Broadcast capable
eventManager.subscribe(EventType::NetworkReady, this);
onEvent(const Event& e) handles callbacks
Used by TimerService, GpioHandler, custom logic
EventManager::getInstance().subscribe(mask(EventType::GpioChange), this);
TRACE("[Controller] Subscribed to GpioChange events\n");
GpioEventManager::getInstance().enableInterrupt(15, GPIO_IRQ_EDGE_RISE | GPIO_IRQ_EDGE_FALL);

## Slide 16: Event Handling
void Controller::onEvent(const Event& event) {
switch (event.type) {
  case FrameworkNotification::TimerTick:
  _state = WAITING_FOR_PROGRAM;
  break;
case FrameworkNotification::RunProgram:
handleRunProgram();
break;
case FrameworkNotification::ProgramStartTime:
handleStartTime();
break;
case FrameworkNotification::ZoneEndTime:
handleZoneEnd();
break;
case FrameworkNotification::GpioChange:
::handleGpioEvent(event);
break;
…

## Slide 17: TimerService
Supports one-shot and recurring timers
scheduleAt(timestamp, EventType::StartZone)
scheduleDailyAt("06:00", EventType::PumpOn)
Backed by RTC or AON time (external RTC support coming)

## Slide 18: Storage Support
SD card file serving via FatFs using 4-bit SDIO (or SPI)
Upload via multipart/form POST (single file only)
JsonService for config/model persistence
All file logic can be excluded at build time [exclusion being worked on right now]

## Slide 19: HTTP Client
HttpRequest with fluent builder API
Full URL parsing with .setUri()
TLS support with root certificate verification
HttpResponse object with status, headers, body, file-saving
Chunked transfer decoding
HttpClient abstraction under-the-hood
printf("\nTLS test to Raspberry Pi example\n");
response = request.setRootCACertificate(BROWSER_ROOT_CA)
.get("https://fw-download-alias1.raspberrypi.com/net_install/boot.sig");
if (!response.ok()) {
printf("RPi Failed to fetch data\n");
}
else{
printf("TLS request sent successfully\n");
printf("RPi Response: %s\n", response.getBody().c_str());
}

## Slide 20: Http Client Fluent Builder
  Build your request:
  request.setHost("httpbin.org")
  .setProtocol("http")
  .setUri("/get")
  .setMethod("GET")
  .setUserAgent("PicoFramework/1.0");
  Send and check for success:
  response = request.send();
  if (response.ok()) {
  printf("Request sent successfully\n");
  printf("Status: %d\n", response.getStatusCode());
  printf("Body:\n%s\n", response.getBody().c_str());
  } else {
  printf("Plain HTTP GET failed\n");
  }

## Slide 21: Optional Features
TLS via mbedTLS and altcp (client-side only right now)
JWT authentication and middleware
SD/FatFs file system and upload handling
Enable/disable via CMake options

## Slide 22: Custom Extensions
Add your own Controllers, Services, Models
Support user-defined events and handlers
Flexible logging and tracing system
Designed for adaptation, not lock-in

## Slide 23: Where It Stands
v0.1.0 release nearly complete (target May early release for discussion and feedback)
Includes working HTTP server, HTTP client, eventing, routing, storage, MVC
Roadmap: WebSockets?, OTA?, CLI?
More examples to come

## Slide 24: Get Involved
Open source under MIT license
GitHub: https://github.com/picoframework
Consulting, support, and customization available
Let's build better embedded apps together

## Slide 25: Testing (In Progress)
CppUTest for embedded unit testing
Mocha for end-to-end testing
[Some mocks available for host CppUtest]

## Slide 26: Documentation
Full Doxygen comments for:
Public headers
Core framework classes
Utility functions
File-level doc blocks
More complete docs coming