## Slide 1: PicoFramework
A lightweight application framework for Raspberry Pi Pico W and Pico 2 W

## Slide 2: What is PicoFramework?
A structured C++ framework for embedded development on RP2040
Inspired by modern web frameworks (e.g., Express.js, Nest.js and similar products)
Ideal for building networked, event-driven IoT applications
Open source, MIT license for any use

## Slide 3: Why PicoFramework?
PicoFramework is the first real framework for multitasking application development on microcontrollers in the style of highly capable application frameworks like Express.js
Inspired by application frameworks like Express.js, Nest.js for javascript and Laravel for php
Limited flash and RAM has historically made it hard to replicate these frameworks on microcontrollers
The Pico and particularly the Pico 2 have a significant amount of flash, and the available RAM is enough to support an application framework
PicoFramework adds value to the Pico SDK by utilizing FreeRTOS to provide a multitasking framework that includes out-of-the box HTTP client and server HTTP handling in an easy-to-use manner.

## Slide 4: Designed for:
IoT controllers (e.g., irrigation, HVAC, lighting)
Network-connected sensors and edge devices
Rapid prototyping of connected hardware
Familiarity for C++ developers
Design architecture that is easily understandable
Extensibility

## Slide 5: Features at a Glance
MVC-style application structure with templated views
HTTP server with routing and middleware
JWT authorization and token generation, password hashing
Http Client with fluent builder style requests
Shared Request and Response objects with access to everything
Integral Json support
Pub/Sub event management with broadcast capability
GPIO events may be use notifications, events or both
SD Card or littlefs storage manager with persistent Json support
Time-of-Day scheduler
Abstracted Tcp support over an lwip layer

## Slide 6: PicoFramework Components
Comprehensive but light framework

## Slide 7: Embedded MVC
Model – stores app config (e.g. schedules)
View – serves HTML/JS from SD card (or your own StorageManager like littleFs)
Controller – handles requests and logic
Inspired by Express.js, adapted for C++

## Slide 8: The App
App::App(int port) : FrameworkApp(port, "AppTask", 2048, 1)
{
std::cout << "App constructed" << std::endl;
}
void App::initRoutes() {
// add a simple route – pin and value are variable and parsed into a RouteMatch object supporting
// match.getParam(“pin”) or you can use an ordered list as we do here
router.addRoute("POST", "/api/v1/gpio/{pin}/{value}", [this](HttpRequest& req, HttpResponse& res, const RouteMatch& match)
{ setState(req, res, match.ordered);}); // Lambdas are very descriptive for routes, but you are not required to use them
void App::onStart()
{
static GpioController gpioController(router); // create a FrameworkController
gpioController.start(); // start it
EventManager* eventManager = AppContext::get<EventManager>(); // get the instance of EventManager from AppContext
GpioEventManager* gpioEventManager = AppContext::get<GpioEventManager>(); // same for GpioEventManager
gpioEventManager->enableInterrupt(16, GPIO_IRQ_EDGE_RISE | GPIO_IRQ_EDGE_FALL); // enable interrupts on pin 16
eventManager->subscribe(mask(UserNotification::Heartbeat), this); // This is how to subscribe to user event you have predefined
waitFor(SystemNotification::NetworkReady); // wait for the Wi-Fi - no need to block – you could do it in poll() with timeout
server.start(); // once we have Wi-Fi up, we can start the HTTP server
}

## Slide 9: The App(2)
void App::onEvent(const Event &e) // OnEvent is automatically called for FrameworkControllers (of which App is a special case)
{ // when an event is received in its event queue
if (e.notification.kind == NotificationKind::System &&
e.notification.system == SystemNotification::GpioChange)
{
printf("[App] GpioChange received\n");
printf("[App] Pin = %u, Edge = 0x%X\n", e.gpioEvent.pin, e.gpioEvent.edge);
}
if (e.notification.kind == NotificationKind::User &&
e.notification.user_code == static_cast<uint8_t>(UserNotification::Heartbeat))
{
printf("[App] Heartbeat user event received\n");
}
}
void App::poll() // poll is also called by the FrameworkController so you can easily mix both event driven and polling
{ // in the same controller runEvery(15000, [&]() // utility function to provide a lambda to run at a set frequency
{
printf("[App] Running main polling loop...\n");
Event userEvt(static_cast<uint8_t>(UserNotification::Heartbeat));
AppContext::get<EventManager>()->postEvent(userEvt); }, "logLoop"); // <-- Unique ID for this timer (enables it to be cancelled)
}
}

## Slide 10: Routing System (Express.js-style)
Add routes via router.addRoute(method, path, handler)
REST-friendly: GET, POST, PUT, DELETE
Lambdas or method pointers as handlers
Per-route and global middleware
Path parsing and matching with variables
Built-in /auth route handler for JWT token test (can override)
Route debug printing (adding, handling routes)
router.addRoute("GET", "/info", [](Request &req, Response &res) { res.sendText("System Info Page"); });
router.addRoute("POST", "/config", configHandler, {authMiddleware});

## Slide 11: Response Handling
res.setStatus(401).send("{\"error\":\"Unauthorized\"}");
Or via helper
JsonResponse::sendError(res, 401, "INVALID_TOKEN", "Invalid token");
void sendError(HttpResponse& res, int statusCode, const std::string& code, const std::string& message) {
  json j = {
    {"success", false},
    {"error", {
    {"code", code},
    {"message", message}
  }}
  };
res.status(statusCode).json(j);
}

## Slide 12: Middleware and Auth
Support for per-route and global middleware:
router.addRoute(GET, "/auth", authMiddleware, &AuthController::handle);
JWT-based authentication with token verification and generation
Optional at build time via PICO_HTTP_ENABLE_JWT

## Slide 13: JWT Authentication
Middleware-based token checking
Authorization: Bearer <jwt> parsing
HMAC signature validation
[Token expiry verification]
Protected route support with fallback 401 response
JWT secret from build or config

## Slide 14: Event System
The Event Management system follows a full pub/sub paradigm
Post and subscribe to system-wide events (waitFor or subscribe/onEvent)
Post and subscribe to user events (subscribe/post/onEvent)
Broadcast capable – all listeners to an event will receive the event
onEvent(const Event& e) handles callbacks
Used by TimerService, GpioHandler, custom logic

## Slide 15: Event Handling
enum class UserNotification : uint8_t {
RunProgram,
ZoneEndTime,
Heartbeat
};
void Controller::onEvent(const Event& event) {
if (event.notification.kind == NotificationKind::User) {
switch (event.notification.user_code) {
case UserNotification::HeartBeat:
_state = WAITING_FOR_PROGRAM;
break;
case UserNotification::RunProgram:
_state = RUNNING_PROGRAM;
handleRunProgram();
_state = WAITING_FOR_ZONE_END
break;
case UserNotification::ZoneEndTime:
handleZoneEnd();
_state = WAITING_FOR_PROGRAM
break;
default:
break;
}
}
}

## Slide 16: TimerService
Supports one-shot and recurring timers
scheduleAt(timestamp, EventType::StartZone)
scheduleDailyAt("06:00", EventType::PumpOn)
Backed by RTC or AON time (external RTC support coming)

## Slide 17: Storage Support
SD card file serving via FatFs using 4-bit SDIO (or SPI) OR littlefs in flash
Upload via multipart/form POST (single file only), Http Responses can be directed to storage
JsonService for config/model persistence
Abstract StorageManager means no change to the application when swapping between littlefs and FATFs

## Slide 18: HTTP Client
HttpRequest with fluent builder API
Full URL parsing with .setUri()
TLS support with root certificate verification
HttpResponse object with status, headers, body, file-saving
Chunked transfer decoding
HttpClient abstraction under-the-hood
printf("\nTLS test to Raspberry Pi example\n");
response = request.setRootCACertificate(BROWSER_ROOT_CA)
.get("https://fw-download-alias1.raspberrypi.com/net_install/boot.sig");
if (!response.ok()) {
printf("RPi Failed to fetch data\n");
}
else{
printf("TLS request sent successfully\n");
printf("RPi Response: %s\n", response.getBody().c_str());
}

## Slide 19: Http Client Fluent Builder
  Build your request:
  request.setHost("httpbin.org")
  .setProtocol("http")
  .setUri("/get")
  .setMethod("GET")
  .setUserAgent("PicoFramework/1.0");
  Send and check for success:
  response = request.send();
  if (response.ok()) {
  printf("Request sent successfully\n");
  printf("Status: %d\n", response.getStatusCode());
  printf("Body:\n%s\n", response.getBody().c_str());
  } else {
  printf("Plain HTTP GET failed\n");
  }

## Slide 20: Optional Features
TLS via mbedTLS and altcp (client-side only v0.1)
JWT authentication and middleware
SD/FatFs file system vs littlefs
Enable/disable via CMake options
Http Client
TLS certificate verification

## Slide 21: Custom Extensions
Add your own Controllers, Services, Models
Support user-defined events and handlers
Flexible logging and tracing system
Designed for adaptation, not lock-in

## Slide 22: Where It Stands
v0.1.0 release nearly complete (target May early release for discussion and feedback)
Includes working HTTP server, HTTP client, eventing, routing, storage, MVC
Roadmap: WebSockets?, OTA?, CLI?
More examples to come

## Slide 23: Testing (In Progress)
CppUTest for embedded unit testing
Mocha for end-to-end testing
[Some mocks available for host CppUtest]

## Slide 24: Documentation
Full Doxygen comments for:
Public headers
Core framework classes
Utility functions
File-level doc blocks
More complete docs coming

## Slide 25: Get Involved
Open source under MIT license
GitHub: https://github.com/picoframework
  Site not public yet
Consulting, support, and customization available
Let's build better embedded apps together